Equations of state for phase transitions in the early universe
Mika Mäki
2022-04-27

---
Outline
- Background and context
  - The early universe and Higgs mechanism
  - Phase transitions and gravitational waves
- Relativistic hydrodynamics and combustion
  - Bubble walls and fluid velocity
  - Equations of state

---
Timeline of the Big Bang
Epoch	Time (s)	T (K)	T (GeV)	Description
Planck epoch	< 10⁻⁴³	> 10³²	> 10¹⁹	???, quantum gravity?
Grand unification epoch	< 10⁻³⁶	> 10²⁹	> 10¹⁶	Grand unified theories?
Inflationary epoch?	< 10⁻³²	10²⁸~10²²	10¹⁵~10⁹	Inflation, exact temperature range unknown
Electroweak transition	10⁻¹²	10¹⁵	~150	Higgs mechanism
QCD transition	10⁻¹²~1	10¹⁵~10¹⁰	150 GeV ~ 1 MeV	Quarks form hadrons
Big bang nucleosynthesis	10~10³	10⁹~10⁷	100 keV ~ 1 keV	Hydrogen & helium production
Recombination	18 kyr ~ 370 kyr	4000	0.4 keV	Cosmic microwave background

---
Higgs mechanism: from massless to massive
Temperature decreases
- Energetically optimal to break symmetry
- Higgs field obtains a vacuum expectation value
- Particles obtain their rest masses by the Yukawa couplings
rest mass for A
Wikimedia Commons, CC BY-SA 3.0
Hindmarsh et al., 2021
TODO: Bump between the minima means a first-order phase transition. Put another plot without the bump and a question mark in between
\begin{align*} \mathcal{L} &= -\frac{1}{4} (F_{\mu\nu})^2 + |D_\mu \phi |^2 - V(\phi) \quad \large| D_\mu = \partial_\mu + ieA_\mu \\ &= ... \\ &= -\frac{1}{4} (F_{\mu\nu})^2 + (\partial_\mu \phi)^2 + e^2 \phi^2 A_\mu A^\mu - V(\phi) \\ \end{align*}

---
Many extensions of the Standard Model result in first-order phase transitions
- Can help in solving
  - Dark matter
  - Electroweak hierarchy problem:
    Why is the Higgs mass only 125 GeV?
  - Baryogenesis: matter-antimatter asymmetry
- Examples
  - Additional singlet scalar fields
  - Electroweakly charged scalar fields: two Higgs doublets etc.
  - Supersymmetry (non-minimal, e.g. minimal + singlet)
  - Extra dimensions
  - (Dark sectors)
- Change of the critical point in the phase diagram
Temperature
Hindmarsh et al., 2021
Higgs mass

---
First-order phase transition proceeds by bubbles
- Sharp boundary
- In our case the transition is from a high-temperature phase to a low-temperature phase
- If strong enough, the sound waves generate gravitational waves
- ”Listening to the noise of a cosmic kettle”
- https://www.youtube.com/watch?v=mfGL8CpORPA
Speeding up the video:
ffmpeg -i "Infant universe blows bubbles [mfGL8CpORPA].webm" -filter:v "setpts=PTS*24/60,fps=60" -an "out.mp4"
Figure source:
https://pixabay.com/photos/water-heater-glass-water-blow-357186/

---
Gravitational waves
- Weak coupling with matter
  → Early universe is transparent
- Production steps in phase transitions
  - Bubble collision and merger
  - Expansion of fluid kinetic energy shells: sound waves
  - Turbulence: non-linearities, sound waves → shocks
- GW mathematics omitted from this presentation
- Isotropic background signal
  - The galactic white dwarf foreground etc. is expected to vary → distinguishable
- Detection: LISA in mid-2030s
Hindmarsh et al., 2021

---
Relativistic hydrodynamics
- [Ultra]relativistic plasma
- Unlike classical fluids: non-conserved particle number
- Characterised by an equation of state
- State given by the energy-momentum tensor

---
GW power spectrum is characterized by five key parameters
- GW power spectrum is characterized by
  - Nucleation temperature
  - Phase transition strength at the nucleation temperature
  - Bubble wall speed
  - Transition rate parameter
  - Sound speed
- Initial analysis: simple toy models
- Goal of the thesis: arbitrary model from particle physics parameters
T_n
\alpha_n
v_\text{wall}
c_s(T,\phi)
\beta

---
Relativistic combustion: self-similar bubbles
- Conservation of energy-momentum at the wall
  - Junction conditions
  - Change in the potential gives kinetic energy to the plasma
- Constant wall speed due to friction
- Relative shape is constant
  = self-similarity
Universe/plasma rest frame
Wall frame
Hindmarsh et al., 2021
\partial^\mu T_{\mu\nu}=0
\begin{align*} w_- \tilde{\gamma}_-^2 \tilde{v}_-^2 + p_- &= w_+ \tilde{\gamma}_+^2 \tilde{v}_+^2 + p_+ \\ w_- \tilde{\gamma}_-^2 \tilde{v}_- &= w_+ \tilde{\gamma}_+^2 \tilde{v}_+ \end{align*}
\xi = \frac{r}{t}

---
Types of relativistic combustion
Black: bubble wall / phase boundary
Color: velocity of moving plasma
Hindmarsh et al., 2021

---
Bag model: the simplest model
- Equation of state:
- The rest can be deduced with thermodynamics
  - Enthalpy density
  - Energy density
  - Entropy density
  - Sound speed
p(T,\phi)
\begin{align*} p_s &= a_s T^4 - V_s \\ p_b &= a_b T^4 \end{align*}
c_s^2 \equiv \left( \frac{\partial p}{\partial e} \right)_s = \frac{1}{3}
\begin{align*} w &\equiv T \frac{\partial p}{\partial T} \\ &= e + p \\ &= Ts \end{align*}
w
e
s
c_s

---
Velocity and enthalpy profiles are different for each type of combustion
Subsonic deflagration:
movement only outside
Supersonic deflagration (hybrid):
movement on both sides
Detonation: movement only inside
Hindmarsh et al., 2021

---
Mathematics: numerical integration
- Compute the velocity profile
  - Start from known boundary conditions
    - and far away
    - at the center of the bubble
  - Integrate numerically
- Use the Sound Shell Model to convert the velocity profile to GW power spectrum
  - Sine transform (a bit like Fourier, numerical integration)
Unphysical: no sound
can propagate here
Symmetric phase
(outside the bubble)
Broken phase
(inside the bubble)
Hindmarsh and Hijazi, 2019
(v,w,\xi)
T=T_\text{nucleation}
v=0
v=0

---
Beyond the bag model
- Assumptions broken
  - Different equations for the phases
  - Different sound speeds, possibly temperature-dependent:
- Computing the velocity profile becomes more difficult
  - Sound speed may change at each point
  - May require nested numerical integration
- Next approximation: Constant sound speed model
  - Different but constant speed of sound in each phase
\begin{align*} p_s &= a_s T^\mu - V_s \\ p_b &= a_b T^\nu \end{align*}
\begin{align*} \mu &= 1 + \frac{1}{c_{s,s}^2} \\ \nu &= 1 + \frac{1}{c_{s,b}^2} \end{align*}
c_s(T,\phi)

---
Goal: Equation of state from an arbitrary model
- Example: Standard Model
- Fluid properties depend on
  - Temperature
  - Phase
- Arbitrary models can be tested, when is given
Data from Borsanyi et al., 2016
g_\text{eff}(T,\phi)
\phi
T
\begin{align*} e(T,\phi) &= \frac{\pi^2}{30} g_e(T,\phi) T^4 \\ s(T,\phi) &= \frac{2\pi^2}{45} g_s(T,\phi) T^3 \end{align*}

---
Summary
- Many extensions of the Standard model result in first-order phase transitions
  → Gravitational waves
- GW power spectrum
  → Velocity profile of bubbles
  → Underlying physics
- Were there first-order phase transitions in the early universe?We will know in the 2030s when LISA is launched.
- If yes, it’s a sign of new physics!

---
Sources
- M. Hindmarsh, M. Lüben, J. Lumma, and M. Pauly, “Phase transitions in the early universe,” SciPost Phys. Lect. Notes, Feb. 2021, doi: 10.21468/SciPostPhysLectNotes.24.
- Hindmarsh, Mark, and Mulham Hijazi. “Gravitational Waves from First Order Cosmological Phase Transitions in the Sound Shell Model.” Journal of Cosmology and Astroparticle Physics 2019, Dec. 2019, doi: 10.1088/1475-7516/2019/12/062.
- Caprini et al. “Detecting Gravitational Waves from Cosmological Phase Transitions with LISA: An Update.” Journal of Cosmology and Astroparticle Physics 2020, Mar. 2020, doi: 10.1088/1475-7516/2020/03/024.
- Espinosa et al. “Energy Budget of Cosmological First-Order Phase Transitions.” Journal of Cosmology and Astroparticle Physics 2010, Jun. 2010, doi: 10.1088/1475-7516/2010/06/028.
- Giese et al., “Model-Independent Energy Budget for LISA.” Journal of Cosmology and Astroparticle Physics, Jan. 2021, doi: 10.1088/1475-7516/2021/01/072.
- Borsanyi, Sz, Z. Fodor, K. H. Kampert, S. D. Katz, T. Kawanai, T. G. Kovacs, S. W. Mages, et al. “Lattice QCD for Cosmology.”, Jun. 2016, ArXiv: 1606.07494